4790 W. 73rd Street

Indianapolis, IN  46268

    - /  317.290.1900 – F

bmaher@aesrack.com

www.aesrack.com

PRODUCT SPECIFICATION

A   1)   ER-130 - ER-130-200/250 or ER-130-215 Air Rotation Units

- FAN - (1) 30” 1/2 hp, 115/1 - 12 amps

- Rated at 9,000 cfm

- Noise level not to exceed 12 sones – 64 dba

- Fan blade galvanized G90 steel minimum 16 gauge – epoxy coated

- hub - keyed to fan shaft

- (7) 32” x 5” front up and down individually pipe locked to reduce blade raw edges

- discharge air blades

- (14) 12” x 5” side up and down individually pipe locked to reduce blade raw edges

- discharge air blades

- (6) 34” x 5” internal left and right individually pipe locked to reduce blade raw edges

- discharge air blades located on the inside of the fan wall assemble

B   1)   ER-230 - ER-230-400/500 or ER-130-430 Air Rotation Units

- FAN - (2) 30” 1/2 hp, 115/1 - 12 amps ea

- Rated at 18,000 cfm

- Noise level not to exceed 12 sones – 64 dba

- Fan blade galvanized G90 steel minimum 16 gauge – epoxy coated

- hub - keyed to fan shaft

- (14) 32” x 5” front up and down individually pipe locked to reduce blade raw edges

- discharge air blades

- (14) 12” x 5” side up and down individually pipe locked to reduce blade raw edges

- discharge air blades

- (12) 34” x 5” internal left and right individually pipe locked to reduce blade raw edges

- discharge air blades located on the inside of the fan wall assemble

Item A & B Unit’s Construction Consists Of:

- A fully assembled wall housing constructed of 20 gauge

- pre-painted Sierra Color-Klad metal with PVC protective coating

- to prevent scratching during installation

- Vibration isolators mounted between fan and fan wall housing

- Primed and painted 3/16” welded angle iron frame - vibration isolators mounted

- between fan wall housing and welded angle iron mounting frame

- OSHA approved front guard located between the fan and the discharge blades

- OSHA approved back guard located between the fan and the inlet of the fan

- discharge air blades located on the inside of the fan wall assemble

- Fan blades anchored with ¼” nylon inset nut and bolts to eliminate loosening

- of the blades during operation

PAGE TWO

Unit’s Mounted Control Panel:

- Constructed out of Pre-painted color-Klad metal

- 10” x 16” bolted to wall housing

- 120/1 service switch mounted on wall housing

- Fan’s ¾ hp motor wired from motor to unit mounted service switch

- 120/1 to 24 volt transformer

- 15 amp motor fuse for motor over-load protection

Remote Control Panel:

- 10” x 8” x 4” electrical enclosure

- 24 volt on/off fan toggle switch with operating with 24 volt operating

- light

- Toggle switch energizes unit heater – unit heater cannot run with out

- Distribution fan running

- 7 day 24 hour 24 volt programmable thermostat

ITEM A:

ER-130-200/250 With (1) 200,000 or (1) 250,000 Btu/hr 80% Unit Heater:

ER-130-215 With (1) 215,000 Btu/hr 93% Unit Heater:

- Primed and painted 3/16” welded angle iron frame - vibration isolators mounted

- between unit heater and welded angle iron mounting frame

- (6) ½ “ pre-punched holes for mounting – unit’s hung with 3/8” all-thread rod

- Unit heater’s welded mounting frame shipped loose (attached to main unit) –

- Both the ER-142 and unit heater frame will have (3) ½” holes punched in frame

- Frames bolted together in the field

- Bolts supplied by ER mfg

Note - Btu/hr and size of unit may vary depending on the unit heater mfg

ER-130 Cooling Unit:

- A fully assembled wall housing constructed of 20 gauge

- pre-painted Sierra Color-Klad metal with PVC protective coating

- to prevent scratching during installation

- Unit Top inlet for supply roof top unit consisting 48” x 20” opening located on the

- top of the unit

- (1) 36” x 22”  back panel to isolate discharge air from roof top unit housing

- constructed of 20 gauge pre-painted Sierra Color-Klad metal with PVC protective

- coating to prevent scratching during installation

- (1) 36” x 14” deflector panel to deflect roof top supply air into ER-142 unit constructed

- of 20 gauge pre-painted Sierra Color-Klad metal with PVC protective coating to

- prevent scratching during installation

PAGE THREE

ITEM B:

ER-230-200/250 With (2) 200,000 or (2) 250,000 Btu/hr 80% Unit Heaters:

ER-230-430 With (2) 215,000 Btu/hr 93% Unit Heaters:

- Primed and painted 3/16” welded angle iron frame - vibration isolators mounted

- between unit heater and welded angle iron mounting frame

- (6) ½ “ pre-punched holes for mounting – unit’s hung with 3/8” all-thread rod

- Unit heater’s welded mounting frame shipped loose (attached to main unit) –

- Both the ER-142 and unit heater frame will have (6) ½” holes punched in frame

- Frames bolted together in the field

- Bolts supplied by ER mfg

Note - Btu/hr and size of unit may vary depending on the unit heater mfg

ER-230 Cooling Unit:

- A fully assembled wall housing constructed of 20 gauge

- pre-painted Sierra Color-Klad metal with PVC protective coating

- to prevent scratching during installation

- Unit Top inlet for supply roof top unit consisting 48” x 20” opening located on the

- top of the unit

- (1) 72” x 22”  back panel to isolate discharge air from roof top unit housing

- constructed of 20 gauge pre-painted Sierra Color-Klad metal with PVC protective

- coating to prevent scratching during installation

- (1) 72” x 14” deflector panel to deflect roof top supply air into ER-142 unit constructed

- of 20 gauge pre-painted Sierra Color-Klad metal with PVC protective coating to

- prevent scratching during installation